PART 1     GENERAL

- SUMMARY

  - Section Includes:

    - All primary and secondary directories, directionals, room identification, workstation ID’s and signage for ADA and life safety code compliance.

  - Related Sections:

    - Division 1:  Administrative, procedural and temporary work requirements.

- REFERENCES

  - Signs and their installation shall comply with applicable provisions of the latest edition of the following standards and with requirements of authorities having jurisdiction:

    - ADAAG – Americans with Disabilities Act Accessibility Guidelines; US Architectural and Transportation Barriers Compliance Board.

    - International Code Council/American National Standards Institute A117.1-Standard on Accessible and Usable Buildings Facilities.

    - National Fire Protection Association 101 Life Safety Code.

- SUBMITTALS

  - Submittals for Review:

    - Signage schedule in manufacturer's format for verification of text/copy.

    - Approval drawings showing materials, construction detail, lay-out, copy, size and mounting methods.

    - Engineering drawings for each sign type.

    - Sample of one sign type for verification of materials, color, pattern, overall quality, and for adherence to drawings and requirements indicated.

- QUALIFICATIONS

  - Manufacturer specializing in manufacturing the products specified in this section with minimum five years experience.  Obtain signs from one source and a single manufacturer.

- WARRANTY

  - Provide manufacturer’s warranty against defects in materials and workmanship for minimum 2 years.

PART 2     PRODUCTS

2.1   MANUFACTURER

- Signage shall be manufactured by:

customADAsign, 1.888-551-0560, www.customadasign.com
Cornerstone Sign & Decal 502-968-8759 www.cornerstonesign.com
or Architect approved equal.

B.	Substitutions:  Bidder must obtain prior written approval from the Architect and/or Owner to bid alternates or substitutions to the specification.

2.2   SIGN STANDARDS

  - It is the intent of these specifications to establish a sign standard for the Owner including but not limited to primary and secondary directories, wall mounted and overhead directionals, flag mounted directionals, primary room identification, restrooms, conference room, work station ID’s and all code compliant signage.

  - Typography:

    - Type style:  see drawings.  Copy shall be a true, clean, accurate reproduction of typeface(s) specified. Upper and lower case or all caps shall be as indicated in Sign Type drawings and Signage Schedule.  Letter spacing to be normal and interline spacing shall be set by manufacturer.

    - Arrows, symbols and logo art:  To be provided in style, sizes, colors and spacing as shown in drawings.

    - Grade II Braille utilizing perfectly round, clear insertion beads.

  - Evacuation Maps:

    - Evacuation maps shall have a unique “you are here” orientation.

  - Color and Finishes:

    - Colors, patterns and artwork:  see drawings.

    - Message Background:  see drawings.

    - Finishes are to meet current federal ADA and all state and local requirements.

2.3   SIGNS

  - Signage System:

    - The signage shall be a direct print acrylic sign system with applied graphics including all tactile requirements in adherence to ADA specifications.

    - Signage shall be capable of accepting direct prints including colors, patterns, graphic images and photography.  Prints shall be second surface to protect from scratches, fading or other damage.

    - All signs, including work station and room ID's, overheads and flag mounts, directionals and directories shall have a matching appearance and constructed utilizing the same manufacturing process to ensure a consistent look throughout.

    - Within the signage system shall be signs with capabilities as follows:

              - signs with raised copy capable of accepting images in designated image areas and changeable printed inserts

              - signs with raised copy and Braille with changeable printed insert

              - signs with raised copy and Braille only

  - Materials:

    - Signage shall be fabricated of acrylic, 1/8” thick or thicker depending on the sign type.  Edges shall be smooth without chips, burrs, sharp edge or marks.  The direct print shall be second surface or underside of the top layer to prevent scratching, fading or other damage.  A top-side print shall not be accepted.

    - Acrylic shall be non-glare optically clear with a P99 finish assuring no loss of clarity or composition of the print.

    - “Glass” looking signs to have a gloss finish.

    - Tactile lettering shall be precision machined, raised 1/32", matte finish colored modified acrylic.

    - The signage shall utilize an acrylic sphere for Grade II Braille inserted directly into a scratch resistant, acrylic face.  Braille dots are to be pressure fit in high tolerance drilled holes.  Braille dots shall be half hemispherical domed and protruding a minimum 0.025".

    - The signage shall utilize a pressure activated adhesive. The adhesive shall be nonhazardous and shall allow for flexing and deflection of the adhered components due to changes in temperature and humidity without bond failure.

    - All signs shall be provided with appropriate mounting tape or hardware.

    - Some signs may be installed on glass.  A blank backer is required to be placed on the opposite side of the glass to cover tape and adhesive.  The backer shall match the sign in size and shape.

  - Colors, Patterns, Imagery and Artwork:

    - All images shall have a minimum resolution of 300 dpi.

    - Face and background colors shall be per the drawings.

    - Standard tactile colors shall match manufacturer's ADA standard color selection.  Font and font colors shall be per the drawings.

  - Printed Inserts

    - The signage shall be capable of accepting paper inserts to allow changing and updating as required.  Insert components shall have a 0.040” thickness non-glare acrylic window and depending on the sign type, shall be flush to sign face for a smooth, seamless appearance.

    - The signage contractor shall be capable of producing all signage inserts.

PART 3     EXECUTION

3.1   DELIVERY, STORAGE, PROTECTION

  - Package to prevent damage or deterioration during shipment, handling, storage and installation.  Products should remain in original packaging until removal is necessary.  Store products in a dry, indoor location.

3.2   EXAMINATION

  - Installer shall examine signs for defects, damage and compliance with specifications.  Installation shall not proceed until unsatisfactory conditions are corrected.

3.3   INSTALLATION

  - General:  Installation locations shall be in accordance with ADA specifications.  Locate signs where indicated using mounting methods in compliance with manufacturer's written instructions:

    - Signs shall be level, plumb, and at heights indicated with sign surfaces free from defects.

    - Upon completion of the work, signage contractor shall remove unused or discarded materials, containers and debris from site.

END OF SECTION